## Slide 1: SMART INDIA HACKATHON 2026
iTantra: Voice That Travels as Meaning
Problem Statement ID – SIH26173
Problem Statement Title – iTantra: Indian Multilingual TTS & STT Aided Neural Transceiver Radio Access for low bitrate links
Organisation – Indian Space Research Organisation (ISRO)
Theme – Miscellaneous
PS Category – Software
Team ID –
Team Name (Registered on portal) – Hexabits
Working prototype
10 languages, offline
Fully open source
iTantra Offline speech-to-speech radio for disasters • 10 Indian languages • ~234 bytes per spoken sentence • runs on 3 GB Android phones
Notes: iTantra turns speech into a tiny signed text packet on the sender's phone, relays it phone to phone over Bluetooth and Wi-Fi Direct, and speaks it again on the receiver. No tower, internet or server.

## Slide 2: iTantra: Send the Meaning, Not the Audio
Hexabits
❖ Proposed Solution (Describe your Idea/Solution/Prototype)
An Android walkie-talkie that turns speech into a few hundred bytes of signed text, relays it phone to phone, and speaks it again on the other side.
1 Speak
Any of 10 Indian languages, push-to-talk or hands-free
2 On-device STT
Silero VAD finds the pause; IndicConformer writes the sentence
3 234 B packet
Text + language + Ed25519 signature, TTL 7
4 Phone mesh
BLE + Wi-Fi Direct relays, up to 7 hops, no tower
5 Spoken aloud
On-device TTS voice; alerts ring at max volume
≈234 B
per spoken sentence
30× smaller
than Opus 16 kbps
120× smaller
than 64 kbps voice
How it addresses the problem
Low bitrate: one sentence is ≈234 B (≈0.5 kbps) instead of >64 kbps streamed audio
No network: phones relay for each other; no tower, internet, SIM or server
Inclusive: people who cannot read still hear the message, in their own language
Low-end ready: int8 models, one language in RAM, runs on 3 GB Android phones
Innovation and uniqueness
Semantic radio
Sends meaning + prosody, not the waveform
Alert-first mesh
Floods all hops; loud until acknowledged
Tamper-proof
Signed packets; encrypted private messages
100% on-device
No cloud API; language packs download once
Notes: Pipeline: speak, on-device STT, a ~234 byte signed packet, phone-to-phone mesh, on-device TTS. The byte figures are measured from our packet format: 22 B header, text, 64 B signature.

## Slide 3: TECHNICAL APPROACH
Hexabits
Technologies to be used
App & UI
Flutter (Dart)
Kotlin (native Android)
Pigeon typed bridge
Riverpod
On-device AI
sherpa-onnx runtime
IndicConformer int8 (STT)
MMS VITS (TTS)
Silero VAD
Mesh & security
BLE GATT mesh
Wi-Fi Direct
Ed25519 signatures
X25519 + ChaCha20
Model tooling
Python
ONNX int8 quantisation
Google Colab
Hugging Face model packs
Methodology and process for implementation (flow)
PHONE A · SENDER
Mic capture
16 kHz mono, echo + noise cancel
Silero VAD
Pause = end of sentence
IndicConformer STT
int8 CTC, one language resident
Packetiser
Sign, fragment, TTL 7
Mesh: verify → dedup → relay with jitter (≤7 hops) → store-and-forward outbox when no neighbour
PHONE B · RECEIVER
Verify + reassemble
Drop unsigned or replayed
MMS VITS TTS
Voice in sender's language
Voice note
Text shown with audio
ALERT mode
Alarm stream, max volume, x3
Working prototype (Android)
Talk · हिन्दी
● STT ready ● Voice ● Offline
हलो हलो
Hindi · STT 236 ms
Or type a message
PTT | Call
236 ms
Hindi sentence decode
644 ms
STT model load
654 ms
TTS voice load
10 / 10
languages verified
Talk screen of the running app (redrawn); timings measured on a OnePlus CPH2717, Android 16.
Notes: Everything runs on the phone: Flutter UI, Kotlin native layer, sherpa-onnx for STT, TTS and VAD. The prototype is running on a OnePlus today; timings on the right are measured on that phone.

## Slide 4: FEASIBILITY AND VIABILITY
Hexabits
Analysis of the feasibility of the idea
10 / 10
languages running fully offline
~0.3 GB
per language (speech + voice packs)
<1.1 GB
peak RAM (est.), fits 3 GB phones
Chart: Round-trip check: character error % by language (lower is better)
| Kannada | Marathi | Tamil | Bengali | Gujarati | Telugu | Odia | Hindi | English | Malayalam
Character error % | 1 | 1.2 | 2 | 3.2 | 3.3 | 3.3 | 6 | 8.5 | 10.2 | 13.6
Each language: our TTS voice speaks a flood warning, our STT transcribes it back (sherpa-onnx, CPU, 2 threads). STT ran 5–20× faster than real time. Next: real speech from 10 speakers per language.
Potential challenges and risks → Strategies for overcoming them
Short range per hop
~60–100 m per Bluetooth hop
7-hop relay, BLE Coded PHY where supported, store-and-forward by moving phones
Hard speech
Noise, soft voices, Malayalam / Odia accuracy
Gain control + tuned VAD, distress hotword list, text shown with voice, real-speech test set
Low-end phones
RAM, battery drain, background kills
int8 models, one language in RAM, duty-cycled scanning, foreground service
Fake alerts and misuse
Spoofing; mesh apps were flagged in India (Jul 2026)
Ed25519-signed packets, verified NDMA / ISRO key, built as an authenticated alert tool
Voice licence
MMS-TTS voices are non-commercial
Swap to CC-BY voices trained on SYSPIN / IndicVoices-R before deployment
Notes: Feasibility is proven, not assumed: the app runs today and all 10 languages pass a round-trip check. RAM figure is an engineering estimate to be replaced with dumpsys meminfo on a 3 GB phone.

## Slide 5: IMPACT AND BENEFITS
Hexabits
85%
of Indians speak one of our 10 languages as mother tongue (Census 2011)
~26%
of Indians aged 7+ cannot read; voice still reaches them (Census 2011)
0
towers, internet, SIM cards or servers needed
₹0
data cost per message, on phones people already own
Potential impact on the target audience
Benefits of the solution
Social
Voice in 10 languages for non-literate, elderly and visually impaired people; no typing needed.
Economic
Runs on existing low-cost phones; zero infrastructure, data or SMS cost; open models.
Environmental
No diesel towers or generators; low-power Bluetooth saves battery in long outages.
Strategic (ISRO)
Byte-sized frames suit NavIC messaging and LoRa links; data never leaves Indian devices.
Next: "heard by N phones" receipts • SMS gateway when any phone regains signal • voice-preserving prosody • 10-phone field trial
Notes: Census 2011: Hindi, Bengali, Marathi, Telugu, Tamil, Gujarati, Kannada, Odia and Malayalam together are ~85% of mother-tongue speakers; literacy 74% means ~26% of people aged 7+ cannot read.

## Slide 6: RESEARCH AND REFERENCES
Hexabits
Details / Links of the reference and research work
Models and tools
AI4Bharat IndicConformer ASR (MIT)
github.com/AI4Bharat/IndicConformerASR
sherpa-onnx: offline speech runtime
github.com/k2-fsa/sherpa-onnx
Meta MMS-TTS voices (VITS)
huggingface.co/facebook/mms-tts
Silero VAD
github.com/snakers4/silero-vad
IndicConformer sherpa-onnx int8 exports
huggingface.co/.../indicconformer-sherpa-onnx
Research
IndicVoices: multilingual Indian speech (ACL 2024)
arxiv.org/abs/2403.01926
STCTS: speech at 80 bps via text + prosody
arxiv.org/abs/2512.00451
IndicVoices-R: Indian TTS corpus (NeurIPS 2024)
github.com/AI4Bharat/IndicVoices-R
BitChat mesh protocol whitepaper
github.com/permissionlesstech/bitchat
SYSPIN: open CC-BY Indian TTS dataset (IISc)
vaani.iisc.ac.in/dataset/syspindataset
Real-world evidence
FireChat mesh, Hong Kong 2014 (500k installs)
en.wikipedia.org/wiki/FireChat
BitChat in Nepal 2025: 48,781 installs in a day
forbes.com (Sep 11, 2025)
Census of India 2011: languages, literacy
censusindia.gov.in
NDMA: disaster management in India
ndma.gov.in
Bridgefy offline mesh adds E2E encryption (2020)
techcrunch.com (Nov 2, 2020)
Our work is open source
Android app, mesh protocol spec and model tooling, plus 20 ready language packs (10 STT + 10 TTS) verified end to end.
App source code
github.com/nileshpatil6/
SIH-Hexabits
Offline model packs
huggingface.co/datasets/
Mr66/itantra-packs
Notes: All links are clickable in the PDF export.