## Slide 1: SMART INDIA HACKATHON 2026
SIH 2026 • PS SIH26173 • ISRO
iTantra
Voice that travels as meaning
Speech in, a 234-byte signed packet across a phone-to-phone mesh, speech out. No tower, no internet, 10 Indian languages, on 3 GB phones.
PROBLEM STATEMENT TITLE
iTantra: Indian Multilingual TTS & STT Aided Neural Transceiver Radio Access for low bitrate links
PROBLEM STATEMENT ID
SIH26173
THEME
Miscellaneous
PS CATEGORY
Software
TEAM ID
TEAM NAME (REGISTERED ON PORTAL)
Hexabits
100% offline
234 B / sentence
10 languages
Alert mode
Notes: iTantra turns speech into a tiny signed text packet on the sender's phone, relays it phone to phone over Bluetooth and Wi-Fi Direct, and speaks it again on the receiver. No tower, internet or server.

## Slide 2: iTantra: Send the Meaning, Not the Audio
Hexabits
01
Proposed Solution (Describe your Idea/Solution/Prototype)
Detailed explanation: speech is recognised on the phone, sent as a few hundred bytes of signed text over a phone-to-phone mesh, and spoken again on the receiving phone.
1 Speak + on-device STT
VAD finds the pause, IndicConformer writes it
2 234 B packet hops the mesh
BLE + Wi-Fi Direct relays, up to 7 hops, no tower
3 On-device TTS speaks it
Voice note; ALERTs ring at max volume
How it addresses the problem: bytes to send one 3.5 s sentence
Raw voice, 64 kbps
28,000 B
Opus codec, 16 kbps
7,000 B
iTantra packet
234 B
120× smaller
No tower, internet or server
Heard by people who can't read
Runs on 3 GB phones
Innovation and uniqueness
Semantic radio
Sends meaning + prosody, not the waveform
Alert-first mesh
Floods all hops; loud until acknowledged
Tamper-proof
Ed25519-signed; private messages encrypted
100% on-device
No cloud API; packs download once
Notes: The bar compares bytes for one 3.5 second sentence: 64 kbps raw voice is 28,000 bytes, Opus 16 kbps is 7,000, our signed packet is 234 bytes (22 B header, text, 64 B Ed25519 signature).

## Slide 3: TECHNICAL APPROACH
Hexabits
02
Technologies to be used
APP & UI
Flutter (Dart)
Kotlin (Android)
Pigeon bridge
Riverpod
ON-DEVICE AI
sherpa-onnx
IndicConformer int8 (STT)
MMS VITS (TTS)
Silero VAD
MESH & SECURITY
BLE GATT mesh
Wi-Fi Direct
Ed25519
X25519 + ChaCha20
MODEL TOOLING
Python
ONNX int8
Google Colab
Hugging Face packs
03
Methodology and process for implementation (flow)
SENDER
Mic 16 kHz
echo + noise cancel
Silero VAD
pause = sentence end
IndicConformer
int8 CTC STT
Packetiser
sign · fragment · TTL 7
MESH verify → dedup → relay with jitter (≤7 hops) → store-and-forward outbox
RECEIVER
Verify
drop unsigned / replayed
MMS VITS TTS
sender's language
Voice note
text shown with audio
ALERT mode
max volume, repeat x3
04
Working prototype (Android)
Talk · हिन्दी
● STT ready ● Voice ● Offline
हलो हलो
Hindi · STT 236 ms
Or type a message
PTT | Call
644 ms
STT model load
236 ms
Hindi sentence decode
654 ms
TTS voice load
10 / 10
languages verified
App screen redrawn from the running build; timings measured on OnePlus CPH2717, Android 16.
Notes: Everything runs on the phone: Flutter UI, Kotlin native layer, sherpa-onnx for STT, TTS and VAD. The prototype runs on a OnePlus today; timings are measured on that phone.

## Slide 4: FEASIBILITY AND VIABILITY
Hexabits
05
Analysis of the feasibility of the idea
10 / 10
languages running fully offline
~0.3 GB
per language: speech + voice packs
<1.1 GB
peak RAM (est.) fits 3 GB phones
Chart: Round-trip test: character error % per language (lower is better)
| Kannada | Marathi | Tamil | Bengali | Gujarati | Telugu | Odia | Hindi | English | Malayalam
Character error % | 1 | 1.2 | 2 | 3.2 | 3.3 | 3.3 | 6 | 8.5 | 10.2 | 13.6
≤5%
5–10%
>10%
Our TTS speaks a flood warning, our STT transcribes it back (sherpa-onnx, CPU). STT runs 5–20× faster than real time.
06
Potential challenges and risks → Strategies to overcome them
Short range per hop
~60–100 m per Bluetooth hop
7-hop relay, BLE Coded PHY where supported, store-and-forward by moving phones
Hard speech
Noise, soft voices, Malayalam / Odia
Gain control + tuned VAD, distress hotword list, text shown with voice, real-speech test set
Low-end phones
RAM, battery drain, background kills
int8 models, one language in RAM, duty-cycled scanning, foreground service
Fake alerts, misuse
Spoofing; mesh apps flagged in India (Jul 2026)
Ed25519-signed packets, verified NDMA / ISRO key, positioned as authenticated alert tool
Voice licence
MMS-TTS is non-commercial
Swap to CC-BY voices trained on SYSPIN / IndicVoices-R before deployment
Notes: Feasibility is shown, not claimed: the app runs today and all 10 languages pass a round-trip check. The RAM figure is an estimate to confirm with dumpsys meminfo on a 3 GB phone.

## Slide 5: IMPACT AND BENEFITS
Hexabits
85%
of Indians speak one of our 10 languages as mother tongue
Census 2011
~26%
of Indians aged 7+ cannot read: voice still reaches them
Census 2011
0
towers, internet, SIM cards or servers needed
fully offline
₹0
data cost per message, on phones people already own
no data plan
07
Potential impact on the target audience
Relief camps
Flooded villages
NDRF / SDRF rescue teams
08
Benefits of the solution
Social
Voice in 10 languages for non-literate, elderly and visually impaired people; no typing.
Economic
Runs on existing low-cost phones; zero infrastructure, data or SMS cost; open models.
Environmental
No diesel towers or generators; low-power Bluetooth saves battery in long outages.
Strategic (ISRO)
Byte-sized frames suit NavIC messaging and LoRa links; data stays on Indian devices.
NEXT "heard by N phones" receipts • SMS gateway on signal • voice-preserving prosody • 10-phone field trial
Notes: Census 2011: Hindi, Bengali, Marathi, Telugu, Tamil, Gujarati, Kannada, Odia and Malayalam together are ~85% of mother-tongue speakers; literacy 74% means ~26% of people aged 7+ cannot read.

## Slide 6: RESEARCH AND REFERENCES
Hexabits
09
Details / Links of the reference and research work
Foundation models
AI4Bharat IndicConformer ASR
MIT
github.com/AI4Bharat/IndicConformerASR
sherpa-onnx offline runtime
Apache-2.0
github.com/k2-fsa/sherpa-onnx
Meta MMS-TTS voices
VITS
huggingface.co/facebook/mms-tts
Silero VAD
MIT
github.com/snakers4/silero-vad
IndicConformer sherpa int8 exports
HF
huggingface.co/.../indicconformer-sherpa-onnx
Academic literature
IndicVoices: Indian speech dataset
ACL 2024
arxiv.org/abs/2403.01926
STCTS: speech at 80 bps (text + prosody)
arXiv 2025
arxiv.org/abs/2512.00451
IndicVoices-R: Indian TTS corpus
NeurIPS 2024
github.com/AI4Bharat/IndicVoices-R
SYSPIN open Indian TTS dataset
IISc
vaani.iisc.ac.in/dataset/syspindataset
BitChat mesh protocol whitepaper
Open
github.com/permissionlesstech/bitchat
Field precedents & data
FireChat mesh, Hong Kong 2014
500k installs
en.wikipedia.org/wiki/FireChat
BitChat in Nepal 2025
48,781 / day
forbes.com/sites/digital-assets
Bridgefy mesh adds E2E encryption
TechCrunch 2020
techcrunch.com/2020/11/02
Census of India 2011
Language, literacy
censusindia.gov.in
NDMA disaster management
Govt. of India
ndma.gov.in
Built, verified and open source
Android prototype
20 language packs
10/10 round-trip
Scan to see the code and download the offline model packs.
App source code
github.com/nileshpatil6/
SIH-Hexabits
Offline model packs
huggingface.co/datasets/
Mr66/itantra-packs
Notes: All links are clickable in the PDF export.